## Slide 1
Sidhan V V
PhD Student
Indian Institute of Technology Delhi
29 Sept 2024
Supervisor: Prof. Manabendra Saharia
Department of Civil Engineering
Indian Institute of Technology Delhi
Spatio-temporal clustering of hydrological extreme

## Slide 2
INTRODUCTION
Streamflow plays a major role in drinking water, agriculture, hydropower and ecosystem
Any variability from expected streamflow will affect the overall water budget of an area.
Extreme variations leads to droughts and floods which pose significant risks to infrastructure and human life.
Their impacts of this floods/ droughts t is more hazardous when
  The events co-occur over a large area (Spatial connectivity)
  Consecutive events occurs over a time window (Temporal clustering)
Understanding the spatial and temporal patterns of these extreme events is crucial for effective water resource management and disaster mitigation.

## Slide 3
INTRODUCTION
Hydrological extremes, such as floods and droughts, often exhibit temporal clustering, where successive events occur in close succession, amplifying their impacts.
Additionally, spatial connectivity between different regions can lead to synchronized hydrological extremes, further exacerbating water crises over large areas
Analyzing the co-occurrence of these events helps in identifying underlying atmospheric drivers, such as large-scale climate oscillations, land surface conditions, and regional weather patterns
A comprehensive understanding of these relationships can improve early warning systems, enhance predictive models, and support adaptive water management strategies in a changing climate.

## Slide 4
Streamflow variability
Atmosphere
Land
Alters water budget
Climate variability
Climate change
Alters energy partition
Human activity
Soil
Geology
Precipitation
Temperature
Solar radiation
Water consumption
LULC degradation
Warming the atmosphere
ENSO, PDO, AMO
Enhance/ depreciate moisture transport
Streamflow variability drivers

## Slide 5
Challenges
PDO +
PDO -
It is challenging to unravel the variability due to natural oscillations and climate change.
A continuous timeseries analysis such as trend test, Mann kandal, correlations etc wont work here as hydrological timeseries are non-stationary.
Temporal drought clustering should be considered in trend analyses where drought-rich periods at the beginning or end of a time series might lead to the detection of artificial decreasing or increasing trends, respectively
Q1. Is this a trend or a part of natural cycle ??
Q2. If this a trend – Is it due to land changes or due to atmosphere changes (global warming)

## Slide 6
Spatial connectivity and temporal clustering of hydrological extremes and their land-atmospheric drivers
Spatial connectivity
Temporal clustering
Hydrological Event Synchronization

## Slide 7
Scopes
Investigate if there is any flood/ drought clustering in streamflow timeseries over India
Study the factors governing the clustering – ENSO, EQUINOO etc
Identify the stations with similar event co-occurring over the time.
Evaluate if there is any hydrological dipoles
Analyse the physical processing governing their co-occurrence
Temporal clustering
A
B
C

## Slide 8: Objective
To investigsa

## Slide 9: Slide 1
Drought flood types
Reference:
Literature Review
Temporal clustering
Spatial-connectivity
Physical Linkage
Different Method

## Slide 10: Slide 1
Reference:
Flood-drought type
1
POT approach
Flood event are classified into 5 categories based on shape of hydrograph
3D drought characterization
Drought centroid tracking
LR
Lun et al., 2020
Fischer et al., 2022
Feng et al., 2024

## Slide 11: Slide 1
Reference:
Flood categories
After extracting flood event based on POT of monthly timeseries, it can be categories to 4 groups based on shape of hydrograph or the governing factor
Here we require the daily timeseries of streamflow, precipitation, p-pet, snowmelts, soil moisture etc etc
So, we can attribute flood based on the factors governing it

## Slide 12: Slide 1
Reference:
LR
Temporal Clustering
Lui & Zhang., 2017
Manuela & Stahl, 2023
Assume flood is a random poison process
We evaluate the independence of poison process over time.
Hydrological droughts show substantially more temporal clustering than meteorological droughts because of memory introduced through different storage and land-surface processes
Different categories of floods is there depending on rainfall runoff behavior, snow melt etc
Fischer., 2022
2
Chagbas et al., 2022
Droughts‐rich periods are more frequent in shorter time scales (several years to one decade) and flood‐rich periods in longer time scales
Lun et al., 2020
sas

## Slide 13: Slide 1
Reference:
It is challenging to unravel the variability due to natural oscillations and climate change.
A continuous timeseries analysis such as trend test, Mann kendal, correlations etc wont work here as hydrological timeseries are non-stationary.
It is challenging to attribute trend to lulc changes or global warming
Temporal clustering

## Slide 14: Slide 1
Reference:
LR
Lui & Zhang., 2017
Lun et al., 2020
Poison distribution
Cox regression model (intra-annual clustering)
Inter-annual clustering (Dispersion index & Kernal occurrence estimation)
Manuela & Stahl, 2023
Applied dispersion & Replays coefficient on streamflow, E-Ep and precipitation data
Boot strapping for significant test
Temporal Clustering (Methods)
2
Scan statistics
Poisson modeling

## Slide 15: Slide 1
Reference:
Ripley’s K
Dispersion Method
Different methods of temporal clustering

## Slide 16: Slide 1
Reference:
Different methods of temporal clustering
Firstly, the index of dispersion, which quantifies the departure from a homogeneous Poisson process, is investigated

## Slide 17: Slide 1
Reference:
LR
Spatially connected events
Spatial flood dependence varies regionally and seasonally
Land‐surface processes are crucial in shaping the spatiotemporal characteristics of flood events apart from meteorology
3
Brunner et al., 2020

## Slide 18: Slide 1
Reference:
LR
Physical linkage
Lui & Zhang., 2017
Utilized vertical velocity

## Slide 19: Slide 1
Reference:
Whether and how hydrological droughts cluster temporally in different hydro-climatic regions across the globe
Whether and how the temporal clustering of hydrological droughts varies between natural and regulated catchments,
how the temporal clustering of hydrological drought relates to the clus tering behavior of meteorological drought
We hypothesize that flood clustering in Germany is mainly caused by catchment memory effects along with intra- to inter-annual climate variability, and that decadal climate variability plays a minor role
Check the case of consecurigve flooding event kerala, 2018,2019
Based on the usual iid (independent, identically distributed) assumption of flood frequency analysis, the T-year flood quantile is assumed constant in time. However, temporal clustering may introduce serial correlation in the flood time series and invalidate the independence assumption
sa
Potential Objective

## Slide 20: Slide 1
Reference:
Potential Objective
Clustering
Spatial
co-occurrence
Temporal dependency
Investigate the regions where there is multiple drought coming together or flood come after drought or normal situation is coming after drought etc.
Investigate if there is significant connectedness in flood events over different stations over India
To explore whether the connectedness is predominant in some specific season
Investigate whether the hydrological connectedness is more than meteorological
Identify seasons and regions where precipitation is insufficient to explain the spatial dependence of floods, where land-surface process must enhance or reduce spatial dependency
To unravel the role of land-surface process over meteorological in flood connectedness
Analyze the asymmetry in flood-drought generation process

## Slide 21: Slide 1
Reference:
Potential Objective
Drivers
Mean precipitation during flood
Mean temperature during

## Slide 22: Slide 1
Reference:
sa
Potential Objective
Date | Station A | Station B | Station C | Station D | Station E | Station F
01/01/2024 |  |  |  |  |  | 
01/01/2024 |  |  |  |  |  | 
01/01/2024 |  |  |  |  |  | 

## Slide 23: Slide 1
Reference:
Whether and how hydrological droughts cluster temporally in different hydro-climatic regions across the globe
Whether and how the temporal clustering of hydrological droughts varies between natural and regulated catchments,
how the temporal clustering of hydrological drought relates to the clustering behavior of meteorological drought
The finding that spatial flood dependencies are governed by both spatial precipitation dependencies and land‐surface processes highlights the importance that these processes must be realistically represented in physical/hydrological models and are present in the initial and boundary conditions used to drive these models
sa
Potential Objective

## Slide 25: Slide 1
Reference:
DATA
DATA | SOURCE | Papers
Human data | ISIMIP2b | Wang et al., 2024 (Anthropogenic climate change..)

## Slide 26: DATA BRANCHING
NO | DATA | Time resolution | Spatial resolution
1 | ILDAS | 1948-2022 (Daily) | South Asia
2 | Gauge station | Random (Daily) | India
3 | PET (GLEAM) | Monthly | World

## Slide 27: DATA BRANCHING
ILDAS Outputs
Gauge data
Metadata.csv
Preprocessing
Select the ILDAS grids matching with gauge station.
Create the streamflow station netcdf
Calculate drought flow and wet flow indices
Identify the grids satisfying the condition of minimum 30 years of data etc
Modify the gauge information csv.
Combine the gauge data of different station to .nc.
Calculate the dry and wet flow indices and save as .nc
IMD-gauge(i)csv’s
Trend_analysis
ILDAS_station_streamflow
ILDAS_station_indices
Gauge_streamflow.nc
Gauge_indices.nc
Gauge_info_p.csv
Trend analysis for each season for all grids has been calculated
Quadrent-based trend classification
ILDAS_indices_trend.nc
Gauge_indices_trend.nc
NO | DATA | Time resolution
1 | ILDAS | 1948-2022
2 | Gauge station | Random
3 |  | 

## Slide 28
Minimum length 30 years
Minimum end period 2010
Total entries/expected entries > 0.8 (bcoz all the dates in b/w starting and end dates doesn’t have data. So expected entries = total length if all dates have data
Criteria (Trend analysis)
Metadata.csv : it contains all the station information : station name, data period length, lat, lon etc
IWM-gauge-1.csv : it contains the timeseries of streamflow and level
1. Modification of start and end datea as they are currently based on stream level.
There area lot of missing data in the time series and all the station doesn’t have sufficient data to do trend analysis
2. Based on the criteria's,the total stations of around 1160 is subsetted to 243
Level data columns are removed and the index are modified according to streamflow .
Gauge_info_p : Start date & end date corrected
Stations subsetted based on criterie
Gauge_streamflow & Gauge_indices
The separate station csvs are merged into a single .nc
Processed data
Data preprocessing Gauge

## Slide 29
ILDAS CALIBERATED ROUTING OUTPUT (Daily)
1. Extract the data only for those grids where gauge stations are location
2. Grid wise data analysis
Processed data
ILDAS station streamflow.nc
Merged into a single xarray dataset
This file is so huge so that memory error will come when we load the data or do any computation. So
ILDAS station Indices.nc
MEMORY ISSUE !!
Calculation of streamflow index (drought flow and flood flow)
Data preprocessing ILDAS data

## Slide 31
1. Checks
0.Datapreprocessing
2.Basic statistics
3. Trend Analysis
Data conversion :
Data synthesis
Data scanning : Investigated the flaws or discreprencies in RE data
Final code : Sorting all the data inconsisties and producing preprocessed outputs
LIS output are in kg/m^2/s. It is a daily average. We Average this daily average over all days in each month to get monthly average. Finally we have the monthly data of each LIS forcing. LIS*60*60*24*30 = mm/month
ANALYSIS STRUCTURE
Gauge data consistency
ILDAS vs Gauge data
Timeseries visualization
Covariance among stations

## Slide 32
1. Gauge data scanning
2. Gauge vs ILDAS comparison
Here we checked the nan values,
Number of zeroes values
1. Distance between Guage and ILDAS grids
2. Streamflow and streamflow index correlation
2. Drtflow flood flow statistics
Drt flow always nan values or zero. Why?
2_Checks

## Slide 33
Results – gauge data consistency

## Slide 34
Results – ILDAS vs Gauge
ILDAS output is gridded while gauge output is station-wise. So we select those grids corresponding to the location where the gauge exists. The grid might not exactly coincide with the gauge station; in that case, the nearest grids are taken.

## Slide 35
Results – ILDAS vs Gauge

## Slide 36
Results – ILDAS vs Gauge

## Slide 37
Results – Streamflow GIFS (40 station of higher correlation)

## Slide 38
Results – Flood flow GIFS (40 station of higher correlation

## Slide 39
Results – Flood flow GIFS (40 station of higher correlation

## Slide 41
We need to add more independent indices
  Seasonality index (Apportionment Entropy (AE))
Discussion
(1) More independent index

## Slide 42
Flood‐rich and drought‐rich periods are defined by when the occurrence of floods and droughts within a time window deviates from a reference condition of independently and identically distributed series
Discussion
(2) Flood rich – Drought rich

## Slide 43
METHODOLOGY SCRAP
HydroSense Lab, IIT Delhi
Develop a consistent index which can capture both flood and drought
Identification of flood-drought transition events over different basins of India (SWAP, EDI)
Investigate the drivers of flood-drought transition
Merge the concepts of Zhao et al., 2020 (flood-drought transition) and Brunner et al., 2020 (dependency)
We use our 3d framework to capture spatio-temporal events (May be this time use a cnn-lstm framework to capture the spatio-temporal drought)
So AI method to capture drought-flood patterns
A consistent index and an adequate timescale is very important (2-4 week)
Findings

## Slide 44
Ideas
Land alteration
Stream flow = atmosphere + land surface
Precipitation is a highly localized and complex phenomenon. So atmosphere variables give a stable quantity to study the long term variability of streamflow
Atmosphere condition and land surface conditions are related
For a particular region, which factor contribute more to streamflow variability : 1. Atmosphere variation
2. Land surface variation

## Slide 45
Continuation
HydroSense Lab, IIT Delhi
Some Indices explored : SPESMI (Standardized Precipitation PET Soil moisture index), SWAP
A consistent index and an adequate timescale is very important (2-4 week)
Findings

## Slide 46
Scopes